## Slide 1: Beam diagnostics for high brightness beams at FACET-II
Doug Storey
SLAC National Accelerator Laboratory
Laser-Plasma Accelerator Workshop 2019 – Diagnostics WG
May 8, 2019

## Slide 2: Acknowledgements
SLAC: C. Emma, M. Hogan, B. O’Shea, G. White, V. Yakimenko

## Slide 3: FACET-II: A National User Facility Based on High-energy Beams and Their Interaction with Plasmas and Lasers
10 GeV e- & e+ beams, 2nC/1nC @ 30/5Hz, ~µm emittance, Ipk > 10kA

## Slide 4: PWFA Research Priorities at FACET-II
Emittance Preservation with Efficient Acceleration
FY19-21
High Brightness Beam Generation & Characterization
FY20-22
Positron Acceleration
FY22-24
Simultaneous Delivery of Electrons & Positrons
FY22-25
10’s nm emittance preservation is necessary for collider apps
Ultra-high brightness plasma injectors may lead to first apps
Positron Acceleration on Electron Beam Driven Wakefields
Stage 1
Stage 1
Stage 3
Stage 2
High-gradient high-efficiency (instantaneous) acceleration has been demonstrated @ FACET
Full pump-depletion and emittance preservation at µm level planned as first experiment
Only high-current positron capability in the world for PWFA research will be enabled by Phase II
Develop techniques for positron acceleration in PWFA stages

## Slide 5: FACET-II Experimental Area – Beam Parameters
Final bunch compressor
Final focus quadrupoles
Spectrometer quadrupoles
Spectrometer dipole
Plasma source
Transverse deflector
Wiggler Spectrometer
Electron and gamma diagnostics
Experimental laser
Notch collimator
Parameter | Single Bunch | Two Bunch Witness/Drive | 
Final energy | 10 GeV | 9.9 | 10.1 GeV
Bunch charge | 2 nC | 0.5 | 1.5 nC
Rep. rate | 1-30 Hz |  | 
Emittance, * | 46, 4.4 µm | 3.2, 2.6 | 21, 37 µm
Max peak current | 165 kA | 28 | 68 kA
at plasma | 5 cm |  | 
at plasma* | 8.2, 3.8 µm | 3.0, 2.6 | 6.3, 9.1 µm
Parameter | Single Bunch | Two Bunch Witness/Drive | 
Final energy | 10 GeV | 9.9 | 10.1 GeV
Bunch charge | 2 nC | 0.5 | 1.5 nC
Rep. rate | 1-30 Hz |  | 
 | 46, 4.4 µm | 3.2, 2.6 | 21, 37 µm
Max peak current | 165 kA | 28 | 68 kA
 | 5 cm |  | 
 | 8.2, 3.8 µm | 3.0, 2.6 | 6.3, 9.1 µm
Beam parameters after final compression:
* = core values
The FACET-II experimental area is configurable to meet the needs of many experiments, including the delivery of:
single and double bunch, high peak current beams.
For more details see: FACET-II Technical Design Report SLAC-R-1072

## Slide 6: FACET-II Experimental Area – Diagnostic Devices
Final bunch compressor
Final focus quadrupoles
Spectrometer quadrupoles
Spectrometer dipole
Plasma source
Transverse deflector
Wiggler Spectrometer
Electron and gamma diagnostics
Experimental laser
Notch collimator
Experimental diagnostics devices include:
Wiggler spectrometer to measure pre-plasma energy spectrum
X-band TCAV and EOS for longitudinal profile measurements
BPMs, OTRs, Wirescanner, Toroids, Pyro-bunch length monitor
Imaging spectrometer diagnostics:
  Both high resolution and large FOV electron profile monitors
  Gamma ray radiation diagnostics
Energy Spectrum
Longitudinal
Momentum

## Slide 7: Imaging Spectrometer Diagnostics
Well equipped spectrometer with both electron and gamma radiation diagnostics:
  Electron diagnostics:
    High resolution profile monitor
    Large FOV profile monitors
    Cherenkov light camera
  Gamma radiation diagnostics**:
    High resolution phosphor screens
    Stack calorimeter
    High precision diagnostics:
      Bent crystal spectrometer
      Compact Compton spectrometer
      Pair spectrometer
** Recall Pablo San Miguel’s talk from Tuesday at 15:20

## Slide 8: Butterfly Emittance Diagnostic
Reimaging Triplet
Spectrometer Dipole
Plasma Source
In-vacuum OTR
Profile Monitor
Butterfly emittance measurement technique:
  Beam is reimaged from waist at plasma exit, to a screen after a spectrometer dipole
    magnifies the beam in
    for a reference energy, for
  Beam size varies with energy
Distance from plasma [m]
Transverse Beam Profile
Weingartner et. al, PRST AB 15, 111302 (2012)

## Slide 9: Butterfly Emittance Measurement
  Beam width at the imaging plane:
  For FACET-II PWFA parameters, minimum beams size is µm for a 3 µm emittance witness beam
      Need good imaging resolution
      No windows
Butterfly Image: µm, cm
Emittance Resolution Estimate

## Slide 10: Extreme beams at FACET-II
FACET-II beams will provide unprecedented beam intensities:
  Sub-10 µm spot sizes and >100 kA peak current
    Heating caused by image currents increases the temperature within the skin depth (G. Stupakov, SLAC-PUB-15729)
No beam windows  Differential pumping required
No diagnostics near the IP  Need new diagnostic techniques
Virtual diagnostic: machine learning based phase space reconstruction
  C. Emma (SLAC)
Edge radiation diagnostic: interference pattern quantifies emittance
  B. O’Shea (SLAC)
Quadrant EOS: measure r-t beam correlations
  M. Litos (CU Boulder)
60 µm
Damage to OTR
µm
µm
Ti heating by 2 nC bunch
New non-intercepting diagnostics are being developed to provide diagnostics of the beam in a challenging environment

## Slide 11: Virtual Diagnostics for High Brightness Beams Slide credit: C. Emma
Shot-by-shot information about LPS important to understanding experiments.
“Virtual diagnostic” is a ML-based computational mapping that predicts the LPS from non-destructive measurements.
Simulation studies and proof-of-concept experiments have demonstrated initial capabilities.
Data taken at LCLS used to build experience and focus effort
LPS
prediction
From ML diagnostic
True
LPS from TCAV
FACET-II
Simulations
135 MeV
335 MeV
4.5 GeV
10 GeV
TCAV
400 A
3.5 kA
10-200 kA
240 A
2 nC
L1 volt.
L1 phase
L2 volt.
L1 phase
L3 volt.
L3 phase
ML based virtual diagnostic
Non-destructive measurements of e-beam and linac parameters
ML-diagnostic provides information about beam that is otherwise unavailable
LCLS data

## Slide 12: Algorithmic Beam Tuning - If you can predict it you can control it Slide credit: C. Emma
Feedback no ML
Target
Feedback + ML
Flow diagram for the ML-diagnostic + feedback
135 MeV
335 MeV
4.5 GeV
10 GeV
400 A
3.5 kA
10-200 kA
240 A
Goal is to decrease tuning time and improve/tailor beam parameters for different experiments - Emittance, Longitudinal Phase Space, Energy…
ML-diagnostic and a feedback algorithm are used to automatically change machine parameters to obtain a desired target phase space
By making an initial guess using the ML-diagnostic, the feedback is able to achieve the desired phase space
Initial
⟲
ML-diagnostic can be used to predict machine settings required to optimize beam delivery
1. Target LPS
2. ML-diagnostic
Feedback
(calculate difference)
Actual LPS
3. Guess machine
settings
LCLS data

## Slide 13: An Edge Radiation Diagnostic for beam measurements Slide credit: B. O’Shea
Quantify emittance and energy spread in a non-destructive manner
Edge Radiation based diagnostics naturally integrates into present linac designs
Diagnostic segments accelerator for better global tuning
Integrates into Gaussian Process, optimizer and other methods
Expect to expand work to positron damping ring
Dipole Magnet
e- trajectory
Dipole Magnet
A single shot, non-intercepting diagnostic ideal for efficient computer control of accelerators
135 MeV
335 MeV
4.5 GeV
10 GeV
400 A
3.5 kA
10-200 kA
240 A

## Slide 14: Summary
FACET-II will start beam commissioning in Fall 2019, and the experimental user program in 2020.
Upgrades from FACET-I will provide orders of magnitude improvements to beam emittance and peak current.
These unprecedented beam intensities create unique challenges for diagnostics of the beam in a challenging environment.
We are planning a FACET-II Science Workshop for Oct 2019:
    For more details contact Mark Hogan, hogan@slac.stanford.edu

## Slide 16
ML-based phase space reconstruction
E-beam from linac
Goal for ML-based virtual diagnostic is to provide shot-to-shot non-destructive measurements of LPS.
Can be used for machine tuning and interpretation of experimental data
Output LPS
ML prediction