## Slide 1
Beam quality optimization in a beam loaded nanocoulomb-class laser wakefield accelerator
Jurjen P. Couperus Cabadağ1
A. Köhler1,2, O. Zarini1,2, R. Pausch1,2, A. Debus1, Y.Y. Chang1, T. Kurz1,2, S. Schöbel1,2, M. Bussmann1, U. Schramm1,2 & A. Irman1
1Institute of Radiation Physics, Helmholtz-Zentrum Dresden - Rossendorf, Germany
2 Technische Universität Dresden, Germany
LPAW, May 2019, Split, Croatia

## Slide 2
Energy spread
Using beam loading to minimize energy spread
Increasing charge:
 energy decrease
 energy spread minimization
Normalized divergence
In this talk
J.P. Couperus et al. Nat. Commun. 8, 487 (2017)
A. Köhler et al., arXiv:1905.02240 (2019)
Peak current
O. Zarini, A. Debus et al., in preparation
Single-shot diagnostic of >10 kA peak current bunches
small energy spread limits betatron phase-mixing

## Slide 3
Energy spread
Using beam loading to minimize energy spread
Increasing charge:
 energy decrease
 energy spread minimization
Normalized divergence
In this talk
J.P. Couperus et al. Nat. Commun. 8, 487 (2017)
A. Köhler et al., arXiv:1905.02240 (2019)
Peak current
O. Zarini, A. Debus et al., in preparation
Single-shot diagnostic of >10 kA peak current bunches
small energy spread limits betatron phase-mixing
See talk Friday

## Slide 4
Stable operation with high charge
Parameters | Mean  Shot-to-shot jitter
Mean peak energy | 250 MeV  22.5 MeV
Charge in fwhm | 220 pC  40 pC
Abs. energy width | 36 MeV  11 MeV
Divergence | 7 mrad  1 mrad
2.5 J, 30 fs, plasma density 3.1x1018 cm-3 , mixed He + 1% N2 , 3 mm gas jet
consecutive shots
A. Irman, J.P. Couperus et al., Plasma Phys. Control. Fusion 60, 044015 (2018)
Ti:Sa Laser DRACO
λ0 = 800 nm
up to 4 J on target
27 fs pulse width (FWHM)
Strehl-ratio > 0.9
20 μm FWHM

## Slide 5
Controlled injection using self-truncated ionization injection (STII)1 of large loads the wakefield
Injected charge can be tuned by concentration of high-z dopant gas
  (0.1 up to 0.5 nC
    in FWHM)
  Systematic study: each data point is acquired by averaging up to 20 shots
Controlled injection of high charge
A. Irman, J.P. Couperus et al., Plasma Phys. Control. Fusion 60, 044015 (2018)
Charge is increased by increasing nitrogen doping
Keep laser parameters constant
 Injection volume phase-space constant
1Zeng et al. Phys. Plasmas 21, 030701 (2014), Mirzaie et al. Sci. Rep. 5, 14659 (2015), Pak et al., PRL 104, 025003 (2010)

## Slide 6
Controlled injection using self-truncated ionization injection (STII) of a large charge (0.1 up to 0.5 nC in FWHM) loads the wakefield.
Stable and reliable operation
Allows for systematic studies, e.g. beam loading, L|PWFA
Theoretical prediction Tzoufras et al.
J.P. Couperus et al. Nat. Commun. 8, 487 (2017)
Optimal beam loading: minimizing energy spread
0.2%
0.5%
1%
1.5%
Maximum electron energy
FWHM energy spread

## Slide 7
Self Truncated Ionization injection
Q_peak = 250 pC
dE = 40 MeV (15%)
Measuring the peak current
CTR spectrometer technique to measure bunch durations
O. Zarini, A. Debus et al., in preparation
O. Lundh et al., Nat. Phys. 7, 219–222 (2011), S.L. Bajlekov et al., PRSTAB 16, 040701 (2013), T. Maxwell et al., PRL. 111, 184801 (2013)
M. Heigoldt et al., PRSTAB 18 121302 (2015), B. Schmidt et al., arXiv:1803.00608 (2018), O. Zarini et al., IEEE AAC (2018)
Was presented in more detail last Monday by Alexander Debus
Large charge + short bunch duration  high current
Coherent Transition Radiation (CTR) spectrometer for
bunch length measurements
time resolution ~ 0.4 fs
single-shot capability
5.5 octaves frequency range
absolutely and relatively calibrated
detection limit ~ 50 fJ

## Slide 8
Operation of a nano-coulomb class laser plasma accelerator
  A tailored STII scheme:
 very robust, good shot-to-shot stability
 control of the injected charge
    (0.1 – 0.5 nC in FWHM)
Conclusion
Outlook
  Experimental results: Next talk by T. Kurz
  Front-to-end simulation: R. Pausch WG4
A hybrid laser- to beam-driven plasma accelerator
LWFA stage:
  Serves as PWFA driver
  high current required (>few kA)
PWFA stage:
  dephasing-free acceleration
  serves as an energy and quality booster
Thank you for your attention!
Pulse length measurements using optical transition radiation
  Peak currents >10 kA