## Slide 1: Upgrading the Cosmic Ray Facility for Tests Regarding the Phase-II Upgrade of the ATLAS Muon Spectrometer
Florian Egli, 14.12.2022
Joint Particle Physics Group Seminar

## Slide 2: Upgrading the Cosmic Ray Facility for Tests Regarding the Phase-II Upgrade of the ATLAS Muon Spectrometer
Florian Egli, 14.12.2022
Joint Particle Physics Group Seminar

## Slide 3: High-Luminosity LHC
[7] https://hilumilhc.web.cern.ch/article/ls3-schedule-change

## Slide 4: ATLAS Muon Spectrometer
[1] The ATLAS Collaboration, The ATLAS Experiment at the CERN Large Hadron Collider (2008)

## Slide 5: Monitored Drift Tubes
From [1]
[1] The ATLAS Collaboration, The ATLAS Experiment at the CERN Large Hadron Collider (2008)
0 V
+3080 V

## Slide 6: Where Can We Test the Upgrade?

## Slide 7: Cosmic Ray Facility

## Slide 8: Cosmic Ray Facility
Why is it not used for Phase-II tests yet?
  Outdated readout electronics (pre Phase-I)
  Outdated infrastructure
 Incompatible Phase-II (and even Phase-I)
 First step: Upgrade the CRF to the Phase-I standard of the Muon Spectrometer

## Slide 9: Upgrading the Cosmic Ray Facility for Tests Regarding the Phase-II Upgrade of the ATLAS Muon Spectrometer
Florian Egli, 14.12.2022
Joint Particle Physics Group Seminar

## Slide 10: Upgrade the Electronics Install New Scintillators

## Slide 11: Upgrade the Electronics Install New Scintillators

## Slide 12: The CRF Electronics
Readout
Configuration
Windows PC
MDT-DCS
CAN-BUS
CSM-Card
25MHz
Jtag
Mezzanine Cards
(x 18)
Linux PC
Optical Fiber
GOLA/FILAR

## Slide 13: Mezzanine
Readout of the MDTs
[5] The ATLAS Collaboration, Technical Design Report for the Phase-II Upgrade of the ATLAS Muon Spectrometer(2017)

## Slide 14: The CRF Electronics
Readout
Configuration
Windows PC
MDT-DCS
CAN-BUS
CSM-Card
25MHz
Jtag
Mezzanine Cards
(x 18)
Linux PC
Optical Fiber
GOLA/FILAR

## Slide 15: CSM
Chamber Service Module
[5] The ATLAS Collaboration, Technical Design Report for the Phase-II Upgrade of the ATLAS Muon Spectrometer(2017)
DCS Analog Mux
GOL (Gigabit Optical Link)
Optical Driver
FPGA Initialization & multiplexing
TTCrx (Trigger Timing & Control)
Optical Receiver

## Slide 16: The CRF Electronics
Readout
Configuration
Windows PC
MDT-DCS
CAN-BUS
CSM-Card
25MHz
Jtag
Mezzanine Cards
(x 18)
Linux PC
Optical Fiber
GOLA/FILAR

## Slide 17: MDT-DCS
DCS: Detector Control System
[3] Y. Arai et al., ATLAS Muon Drift Tube Electronics (2008)

## Slide 18: The CRF Electronics
Readout
Configuration
Windows PC
MDT-DCS
CAN-BUS
CSM-Card
25MHz
Jtag
Mezzanine Cards
(x 18)
Linux PC
Optical Fiber
GOLA/FILAR

## Slide 19: FILAR
Four Input Links for Atlas Readout
Interface between PC and Optical Link
[6] https://hsi.web.cern.ch/s-link/devices/filar/welcome.html

## Slide 20: FELIX
Front-End LInk eXchange
Trigger and Data Acquisition (TDAQ) system
Installed in ATLAS during Phase-I Upgrade
Scalable, detector agnostic and easily upgradable
Compatible to Phase-II Electronics

## Slide 21: FELIX
[4] FELIX User Manual (Version: 4.2.4)

## Slide 22: Upgrade of the CRF Electronics
Readout
Configuration
Windows PC
MDT-DCS
CAN-BUS
CSM-Card
25MHz
Jtag
Mezzanine Cards
(x 18)
Linux PC
Optical Fiber
GOLA/FILAR
FELIX
50 MHz

## Slide 23: The CRF Electronics (Phase-I)
Readout
Configuration
MDT-DCS
CAN-BUS
CSM-Card
50MHz
Jtag
Mezzanine Cards
(x 18)
Linux PC
Optical Fiber
FELIX

## Slide 24: Validation and Verification of the CRF Upgrade
So far installed in a small test setup
How do I validate that I setup the system correctly?
  Step 1: Does it produce data? 
  Step 2: Does the data make sense?

## Slide 25: Step 2.1: Untangle the Data

## Slide 26: FELIX Dataformat
[4] FELIX User Manual (Version: 4.2.4)

## Slide 27: CSM Dataformat
[4] Y. Arai, AMT-3 User‘s Manual (2003)

## Slide 28: Does the Data make sense?
Look at time between trigger and threshold crossing of MDT Signal
Signal Individual MDTs
[4] Y. Arai, AMT-3 User‘s Manual (2003)

## Slide 29: Step 2.2: What should the data look like?

## Slide 30: Garfield++
Garfield++ is a program designed to simulate electron drift and gas amplification
I translated an old Garfield script to the new Garfield++ standard
[1] The ATLAS Collaboration, The ATLAS Experiment at the CERN Large Hadron Collider (2008)

## Slide 31: MDT Drifttime Spectra
Gas Mixture: Ar:CO2 (93:7)
Muons with fixed energy (90 GeV)
Sample from uniform distribution
Plot time difference between muon crossing and signal of MDT into histogram
[1] The ATLAS Collaboration, The ATLAS Experiment at the CERN Large Hadron Collider (2008)

## Slide 32: MDT Drifttime Spectra
[2] The ATLAS Collaboration, Resolution of the ATLAS muon spectrometer monitored drift tubes in LHC Run 2 (2019)

## Slide 33: What does the data actually look like?

## Slide 34: Outlook: Finish the setup of the FELIX system
Optimize configuration parameters of Mezzanines
Compare to Data from old setup
Merge FELIX Datastream with existing Datastream
Expand from Test Setup to a whole MDT-Chamber

## Slide 35: Upgrade of Electronics Install New Scintillators

## Slide 36: Cosmic Ray Facility

## Slide 37: Install New Scintillators
All scintillators now are perpendicular to MDTs
Install new scintillators in parallel MDTs
   This will allow the implementation of a path-based trigger

## Slide 38: Path-Based Trigger

## Slide 39: Summary
Goal: Use CRF as testing site for tests of the Phase-II Upgrade
Problem: Readout Electronics and Infrastructure in the CRF are outdated
Current Project: Upgrade the CRF to Phase-I standard
Next Project: Install new Scintillators and Test Path-Based Trigger on the CRF

## Slide 40: Backup

## Slide 41: Gas Contents

## Slide 42: Gas Contents
Simulations with Water and Oxygen admixture in the Gas: