H8 Beamtime Update
Introduction:
ATLAS New Small Wheel Spare MM was irradiated with a 137Cs source for multiple years to investigate the possible ageing of the detector (HV-stability, gain, resolution, efficiency)
Test Beam campaigns are exploited to investigate these parameters in between irradiation periods
H8 provides a proton/pion beam with 5 cm diameter
Goal:
Scan the whole surface of the detector with the beam
(~70 measurements/voltage setting)
Measurements with the detector under fixed angle (0, 10, 20, 30 deg)

---
Detector Setup
4 Reference Trackers
(40 x 40 cm^2, 1-4)
SM1 M40 Micromegas
2 Szintillators in coincidence as trigger
Desy-table (orange) to move the SM1 M40 to scan the surface
NSW MMFE8 electronics for DAQ
Particle beam (80/20 protons/pions) enters from the left
SM1
3/4
1
2

---
Status
- SPS issues (magnet exchanged) → Switch to cosmic muon setup by tilting the detector for debugging
- One full surface scan for track inclination of 29 deg taken with beam in the night from Tuesday to Wednesday 5am (5 voltages)
- SPS technical stop from Wednesday→Friday (Saturday)

---
Beamprofile
2D profile of the beam
Positional correlation between tracking chambers (300 urad)

---
Cluster Charge SM1
Landau fit of the charge distribution → 150 GeV Pions + Protons → MIPs

---
Track Angle (29 deg set)
Highly preliminary reconstructed track angle:
Gaus + Landau with center at 29.13 and 32.51 respectiveley

---
Ongoing Work
- Analysis of the surface scan → Tedious since multiple alignments have to be done (theoretically at each measurement position ~70)
- Switch back to vertical position on Friday/Saturday and repeat surface scan
- Measurements under 10 and 20 deg